## Slide 1: Map Coordinates Extraction in Video Images
Flat Angles Problem and Possible Solutions
Yoav Rosenberg

## Slide 2: Protrack: Technology and Applications
Video Stabilization and Enhancment
Motion Detection and Classification
Unattended\Abandoned Object Detection
Object Tracking
Exact Coordinates extraction
Geo-referenced Mosaics
For airborne and ground cameras

## Slide 3: Map Coordinates Extraction – based on camera’s physical data
p
P
Given:
Video image
Camera’s GPS approximated position - O
Camera’s approximated Field of View - FOV
Approximated view angles - V
DEM – Digital Elevation Model
The Problem:
Compute the map coordinates P of a pixel p in the video image
Compute the approximated camera model - M
Compute the line of sight going through p
Intersect the line with the DEM and find P
O
V

## Slide 4
very accurate results can be achieved by using a system which matches the image to an Orthophoto (Orthogonal Aerial Photo)
Accurate Camera Model
Approximate Camera Model M
T1,2
Rendered Image
Image Correlator (Image Matching)
T1,2 x M
Map Coordinates Extraction – based on Image Matching
Video Image
Orthophoto + DTM
Renderer

## Slide 5: Continuous Video Matching
Several technics can be used to allow continuous coordinates extraction in real-time video:
Compute the motion between consecutive video frames to predict the camera model in the next frame
If direct video matching failed, previously matched images can be used instead

## Slide 6: Continuous Video Matching - Demo
ProTrack’s MAOF system

## Slide 7: The Flat Angle Problem
Matching a video from a flat angle camera is problematic:
  The Orthophoto is created from a bird’s view angle
  The DEM does not reflect the earth’s cover
Renderer
Rendered Image
Ground Camera
Video Image
Orthophoto
Near- Orthogonal
View Point

## Slide 8: Flat Angle Problem - Example
Original Orthophoto
Rendered View
Ground Camera View

## Slide 9
Build and use a geo-referenced mosaic taken from the observer’s location
1o
0o
-1o
350º
0º
10º
Solving the Flat Angle problem for Fixed Cameras

## Slide 10: Fixed Camera Solution (cont.)
Building the Mosaic

## Slide 11: Fixed Camera Solution (cont.)
Matching the mosaic to the rendered Orthophoto
Orthophoto rendered to the camera viewpoint
Orthophoto

## Slide 12: Fixed Camera Solution (cont.)
1
2
3
4
17
23
M 1,2
M 2,3
M 3,4
M 4,5
M 17, 18
M 16,17
M 23, 24
M I,j transformation matching between images
T17
T23
TI = Successful matching of video frame i to the Orthophoto
Solving the mosaic

## Slide 13: Fixed Camera Solution (cont.)
M I,j
T I
C I =
Appr. Camera position of video frame
Bundle Adjustment
Solved mosaic
Pi,j = Azimuth and Elevation
The mosaic can be solved with relatively sparse matching to the Orthophoto

## Slide 14: Fixed Camera Solution (cont.)
Matching the video to the anchored mosaic

## Slide 15: Orthophoto vs. Anchored Mosaic
Orthophoto
Anchored Mosaic
P I,j  Azimuth & Elevation
Real World
P I,j  X,Y,Z

## Slide 16: Extracting the map coordinates of a pixel in the panoramic view
Given the camera location and view angle, the line of sight is intersected with the Digital Elevation Map (DEM) in order to get the map coordinates
Ground Intersection Point
Elevation
Traverse

## Slide 17: Example
ProTrack’s MAOF system

## Slide 18: Ambiguity in Flat Angles

## Slide 19: Solving Ambiguities with DSM

## Slide 20: Solving Ambiguities without DSM (cont.)
I
Video
Orthophoto
Ambiguity Zone
Using 2 mosaics from different view points (~10o)

## Slide 21: Solving Ambiguities without DSM (cont.)
I
Video
Orthophoto
Ambiguity Zone
I
Search the target along the Epipolar line
Epipolar Line

## Slide 22: Solving Ambiguities without DSM (cont.)
I
Video
Orthophoto
Ambiguity Zone
I

## Slide 23: Solving Ambiguities without DSM (cont.)
I
I
Using an Aerial photo
Aerial photo
Ground Mosaic

## Slide 24: Thank You
Yoav@protrack.co.il